## Slide 1: Implementation of a Configurable Neural Processing Unit with Input & Weight Stationary data flows
Rehan Karthik Chandralal
Matrikel No: 5127834 MS Nano-electronic Systems TU Dresden, Germany
Supervised by
Mr Dr.-Ing. Ahmed Kamaledin Atef
June 26 2024
Institute of Computer Engineering- Chair of Adaptive Dynamic Systems
Research Project - Final Presentation

## Slide 2: Overview
Motivation
Task Description
State of the Art Examples
Architecture Design of NPU
  AXI Interface
  Buffers
  Data Pre-processing Unit
  Interconnect
  PE Array
  Pooling Unit
  Control Unit
Results & Evaluation
Future Scope
Conclusion
References

## Slide 3: Motivation

## Slide 4: Motivation Neural Processing Unit (NPU)
Neural Processing Unit (NPU) is a specialized hardware accelerator that provides:
Optimized output for training & inference tasks of convolutional neural networks
Significant performance improvements from offloading of neural network computations from the CPU
Fig. 1. Convolutional Neural Network [1]
Fig. 2. Offloading of tasks from CPU to NPU [2]

## Slide 5: Motivation Examples of NPU
Apple Neural Engine
      present in iPhones, iPads & Macs
      used for image and speech recognition, natural language processing
Qualcomm Hexagon DSP
  present in Snapdragon processors like 855, 865 & 888
  used for accelerating AI tasks related to camera, voice assistants, and gaming.
Fig. 3. Apple M1 chip with Neural Engine [3]
Fig. 4. Qualcomm 865 with Hexagon 698 [4]

## Slide 6: Motivation Dataflow Techniques
Data movement between several parts of the architecture can consume a large amount of power
Dataflow techniques exploit data reuse to optimize power consumption
Examples:
  Weight Stationary
  Input Stationary
  Output Stationary
  Row Stationary
Fig. 5. Comparison of energy cost of dataflow vs computation [5]

## Slide 7: Motivation Weight Stationary Dataflow
              In weight stationary data-flow, the same weight is broadcasted to all MAC Units
              Data Reuse by weights being stationary across several batches of data
              Use Case: Image recognition tasks using CNNs [Eyeriss] [6]
Fig. 6. Weight Stationary Dataflow [10]

## Slide 8: Motivation Weight Stationary Dataflow
MAC1
MAC2
MAC3
MAC1
MAC2
MAC3
IA.1 W1
IA.3 W3
IA.2 W2
IB.1
IB.3
IB.2
SA.1
SA.2
SA.3
SB.1
SB.2
SB.3
W1
W3
W2
Batch A
Batch B

## Slide 9: Motivation Input Stationary Dataflow
              In input stationary data-flow, the same input is broadcasted to all MAC Units
Data Reuse by inputs being stationary across several batches of data
Use Case: Video processing of multiple frames [Diannao] [7]
Fig. 7. Input Stationary Dataflow [10]

## Slide 10: Motivation Input Stationary Dataflow
MAC1
MAC2
MAC3
MAC1
MAC2
MAC3
I1 WB.1
I3 WB.3
I2 WB.2
WB.1
WB.3
WB.2
SA.1
SA.2
SA.3
SB.1
SB.2
SB.3
I1
I3
I2
Batch A
Batch B

## Slide 11: Task Description

## Slide 12: Task Description
  Create a systolic array architecture for Multiply-Accumulate (MAC) operations
  Design a flexible interconnect to support both weight and input stationary dataflows
  Implement a control unit to orchestrate data transfers based on the chosen dataflow
  Evaluate the developed NPU in terms of execution time, resource utilization and power consumption for the two types of dataflow models

## Slide 13: State of the Art Examples

## Slide 14: State of the Art Examples
MAERI: Enabling Flexible Dataflow Mapping over DNN Accelerators via Reconfigurable Interconnects
MAERI uses tiny switches to adjust how data flows between processing elements
Unused connections are avoided leading to significantly higher resource utilization and potentially better performance compared to rigid architectures
Fig. 8. MAERI Architecture [8]

## Slide 15: State of the Art Examples
2. Flexible Dataflow CNN Accelerator on FPGA
This design uses reconfigurable logic to handle diverse layers and dataflows
Resource utilization is improved by dynamically adjusting its processing pipeline and avoiding unnecessary computations, potentially achieving higher efficiency than fixed accelerators
Fig. 9. Flexible Dataflow CNN Accelerator on FPGA [9]

## Slide 16: Architecture Design of NPU

## Slide 17: Overview of NPU Architecture
AXI Interface
Buffers
Data Pre-processing Unit
Interconnect
PE Array
Pooling Unit
Control Unit
Fig. 10. NPU Architecture

## Slide 18: AXI Interface
              AXI Lite Interface serves two primary functions:
                It receives a data packet per clock cycle from the Core and routes it to the designated buffers (input, weight, or index) in the NPU
                After processing, the system streams elements of the output feature map from the output buffer back to the user
Fig. 11. AXI Interface

## Slide 19: Buffers
Buffers serve as temporary storage units that facilitate efficient data flow management within the NPU
  Input Buffer
  Weight Buffer
  Index Buffer
Fig. 12. Overview of all Buffers
  Input Buffer
  Weight Buffer
  Index Buffer
  4. Output Buffer
INPUT DATA
OUTPUT DATA

## Slide 20: Buffers Types of buffers
  1. Input Buffer
  The input feature map represents the raw data or the input image supplied to the NPU
  Elements of the input feature maps are stored in the input buffer
  2. Weight Buffer
  Weights are the adjustable parameters that are fine-tuned during training to identify important features within the input data
  Elements of the weights matrix is stored in the weight buffer
Fig. 12. Overview of all Buffers

## Slide 21
  3. Index Buffer
  The index buffer allows users to assign input data to specific MAC units
  7 bits are used to represent 81 possible MAC units
  4. Output Buffer
  The output buffer accepts data from the PE array and transfers it to the user via AXI interface
  Stores elements of the final output feature map
Fig. 12. Overview of all Buffers
Buffers Types of buffers

## Slide 22: Data Pre-processing Unit
The input data needs to be processed for the convolution operation
To reduce complexity of PE Array, a separate module named Data Pre-processing unit is used
It receives inputs from the Buffers and supplies processed data to the Interconnect module
Fig. 13. Data Pre-processing Unit

## Slide 23: Data Pre-processing Unit Functions
The Data Pre-processing Unit performs 3 main functions:
  Modifying Input Matrix for Zero padding and different Stride lengths
  Mapping Convolution onto Toeplitz matrix
  Batch division
Fig. 13. Data Pre-processing Unit

## Slide 24: Data Pre-processing Unit Functions-Modifying Input Matrix for Zero padding and different Stride lengths
Dimensions of the input data matrix are adjusted to accommodate
  Zero-padding (increase in dimensions)
  Varying stride lengths (decrease in dimensions)
Zero Padding
extra rows and columns of zeros added around the borders of the input data matrix
Output feature map has same size as input feature map
Fig. 14. Zero Padding [11]

## Slide 25: Data Pre-processing Unit Functions-Modifying Input Matrix for Zero padding and different Stride lengths
Full Padding
  all pixels are visited equal number of times by the filter
  output feature map with increased spatial dimension
Same Padding
  output feature map has the same spatial dimensions as the input
Fig. 15. Full and Same Padding [12]

## Slide 26: Data Pre-processing Unit Functions-Modifying Input Matrix for Zero padding and different Stride lengths
Stride
  increment size used when sliding a kernel across the input data
  Larger stride leads to smaller output feature maps
Fig. 16. Stride = 1 and Stride = 2 [13]

## Slide 27: Data Pre-processing Unit Functions-Mapping Convolution onto Toeplitz Matrix
Convolution operations can be expressed as simple matrix multiplications using the Toeplitz Matrix
Size of Toeplitz Matrix is given by :
Ntoe = (Hin − 2) * (Win − 2) * K
Fig. 17. Convolution using Toeplitz Matrix [14]
Parameter | Description
Ntoe | Total no. of elements in the Toeplitz matrix
Hin | Input Feature Map Height
Win | Input Feature Map Width
K | Kernel Size
Table. 1. Toeplitz Matrix Parameters

## Slide 28: Data Pre-processing Unit Functions-Batch Division
Since the PE array has a size of 9x9, it can only process 81 inputs and weights simultaneously
For input feature map sizes larger than 9*9, it becomes necessary to divide the data into batches

## Slide 29: Interconnect
Array of multiplexers responsible for implementing weight & input stationary dataflow
Out of 162 multiplexers,
  81 multiplexers channel input values to the PE array
  The other 81 multiplexers channel weight values to the PE array
Fig. 18. Interconnect Module

## Slide 30: Interconnect
A control signal determines whether the multiplexer in the interconnect selects data from the input matrix or the weight matrix
This data is fed into a designated MAC unit in the PE array
Fig. 18. Interconnect Module
Control Signal | Mode
00 | Weight Stationary with Unicast
01 | Weight Stationary with Multicast
10 | Input Stationary with Unicast
11 | Input Stationary with Multicast

## Slide 31: Interconnect
      Unicast :- One specific signal is sent to one specific PE
      Multicast :- One signal is sent to one row of PE‘s
      Broadcast :- One signal is sent to all 81 PE‘s
Fig. 19. Types of Communication Modes [14]

## Slide 32: PE Array
It receives inputs (single channel) and weights corresponding to the selected dataflow from the interconnect module and performs convolution
Comprises of 81 MAC units arranged in 9*9 format
As the Kernel size is 3*3, 9 elements of the output feature map are produced for one batch of inputs and weights
Fig. 20. PE Array (systolic)

## Slide 33: PE Array MAC unit
As data streams through the 9 MAC units present in a row of the PE array, one element of the Output feature map is formed
The MAC unit is implemented with the usage of DSP slices on the FPGA
Fig. 21. MAC Unit [15]

## Slide 34: Pooling Unit
              Pooling Operation reduces size of feature maps in order to reduce computational complexity and memory requirements
  Max Pooling selects the maximum value within a predefined window of 2*2
Average Pooling computes the average value in the same window of 2*2
Fig. 22. Max & Average Pooling [16]

## Slide 35: Control Unit
The Control Unit facilitates communication and synchronization between various modules
State Transition is primarily driven by
  input signals such as buffer readiness
  control signals from the user
Fig. 23. Control Unit

## Slide 36: Results & Evaluation

## Slide 37: Results & Evaluation Design Features of the NPU
Convolution Layer Parameters Parameters | Maximum Range
Kernel Size (bits*bits) | 3*3
Data Width | up to 18 bits
Input feature Map size (bits*bits) | from 5*5 to 256*256 (non-square matrix also supported)
No of dataflows | 2 (Input and Weight stationary)
No of communication modes | 3 (Broadcast, Multicast and Unicast)
Stride | 1,2,3,4
Pooling | 2 types (Max and average pooling)
Padding | 2 types (Full and same padding)
Table. 2. Design Features

## Slide 38: Results & Evaluation Clock Info, Resource Utilization & Power Consumption
Clock Period (ns) | Frequency (MHz)
7.1 | 140
Fig. 24. Power Consumption
Fig. 25. Resource Utilization

## Slide 39: Results & Evaluation Detailed Resource Utilization
Fig. 26. LUT Utilization
Fig. 28. DSP & IO Utilization
Fig. 27. Flip Flop Utilization

## Slide 40: Results & Evaluation Simulation
Testcase 1 = Input Stationary with Zero padding
A Simulation was performed on an Input feature map of size =7*7 with control signal = 10 ( Input stationary with Unicast)
Testcase Parameters P | Value
DATA WIDTH | 4
INPUT_WIDTH | 7
INPUT_HEIGHT | 7
KERNEL_SIZE | 3
WEIGHT_HEIGHT | 21
WEIGHT_WIDTH | 21
STRIDE | 1
PADDING | 1
Table. 3. Parameters for Testcase 1

## Slide 41: Results & Evaluation Simulation
Fig. 29. Input Feature Maps & Weights for Testcase 1

## Slide 42: Results & Evaluation Simulation
Fig. 30. Outputs for Testcase 1

## Slide 43: Results & Evaluation Simulation
Testcase 2 = Weight Stationary with Stride = 2
A Simulation was performed on an Input feature map of size =32*32 with control signal = 00 ( Weight stationary with Unicast)
Testcase Parameters P | Value
DATA WIDTH | 8
INPUT_WIDTH | 32
INPUT_HEIGHT | 32
KERNEL_SIZE | 3
WEIGHT_HEIGHT | 3
WEIGHT_WIDTH | 3
STRIDE | 2
PADDING | 0
Table. 4. Parameters for Testcase 2

## Slide 44: Results & Evaluation Simulation
Fig. 31. Input Feature Maps & Weights for Testcase 2

## Slide 45: Results & Evaluation Simulation
Fig. 32. Outputs for Testcase 2

## Slide 46: Future Scope

## Slide 47: Future Scope
Expanding Dataflow Exploration:
  Investigate output- and row-stationary dataflows to further optimize memory access and resource utilization within the NPU
Advanced Interconnect Design:
  Explore the feasibility of incorporating network-on-chip (NoC) principles within the NPU for more scalable communication between PEs, especially for larger array sizes

## Slide 48: Conclusion

## Slide 49: Conclusion
This versatile NPU architecture optimizes dataflows leading to significant performance gains and lower power consumption.
The configurable interconnect and diverse features (stride, padding, pooling) ensure the NPU can handle a wide range of CNN architectures and applications.
The design leverages DSP slices for efficient MAC operations, maximizing resource utilization on the FPGA platform.
Performance analysis across various convolution layer parameters validates the effectiveness of the NPU design.

## Slide 50: References

## Slide 51: References
Convolutional Neural Network https://nafizshahriar.medium.com/what-is-convolutional-neural-network-cnn-deep-learning-b3921bdd82d5
Ravi, Murali & Sewa, Angu & G., Shashidhar & Sanagapati, Siva. (2019). FPGA as a Hardware Accelerator for Computation Intensive Maximum Likelihood Expectation Maximization Medical Image Reconstruction Algorithm. IEEE Access. PP. 1-1. 10.1109/ACCESS.2019.2932647.
Apple M1 chip https://www.techinsights.com/blog/analysis-apple-m1-happening-and-thermal-imaging
Qualcomm 865 chip with Hexagon DSP https://www.edge-ai-vision.com/2021/04/tvm-open-source-compiler-now-includes-initial-support-for-qualcomm-hexagon-dsp/
Comparison of energy cost of Dataflow vs Computation https://allenlu2007.wordpress.com/2019/05/12Architecture-and-energy-efficiency/
Yu-hsin Chen, T. Krishna, V. Sze. "Eyeriss: An Energy-Efficient Reconfigurable Accelerator for Deep Convolutional Neural Networks." In Proceedings of the 43rd International Symposium on Computer Architecture (ISCA '16). IEEE Press, Article 74, June 2016
"DianNao: A Sparse Neural Network Accelerator" by Jungwook Choi et al.
Hyoukjun Kwon, Ananda Samajdar, and Tushar Krishna. MAERI: Enabling Flexible Dataflow Mapping over DNN Accelerators via Reconfigurable Interconnects. 2018.
Haoran Li et al. A Flexible Dataflow CNN Accelerator on FPGA. 2023.
Y.-H. Chen, J. Emer, and V. Sze. Eyeriss: A Spatial Architecture for Energy-Efficient Dataflow for Convolutional Neural Networks. 2016
Serveh Kamrava, Pejman Tahmasebi, and Muhammad Sahimi. Linking Morphology of Porous Media to Their Macroscopic Permeability by Deep Learning. 2019. DOI: 10.1007/s11242-019-01352-5

## Slide 52: References
Avinash Kumar, Sobhangi Sarkar, and Chittaranjan Pradhan. Malaria Disease Detection Using CNN Technique with SGD, RMSprop and ADAM Optimizers. 2023.
Baeldung. Convolutional Neural Network Channels.
Vivienne Sze et al. Efficient Processing of Deep Neural Networks: A Tutorial and Survey. 2020. DOI: 10.1109/JSTSP.2020.3009164.
Jia Chen et al. Multiply accumulate operations in memristor crossbar arrays for analog computing. 2021. DOI: 10.1088/1674-4926/42/1/013104.

## Slide 53: Thank you for your time and patience